# USER MANUAL
# UPS-2 Uninterruptible Power Supply
## Hat Solution For Raspberry Pi Computers
UPS-2 is a wide input range, high efficiency power supply for Raspberry Pi computers. It features a main input and a backup input. In case of power fail or under voltage at the main input, backup input becomes active with no interruption or spike on the Raspberry 5V, 3A supply output.
Firmware provides optical and software state feedback, including voltage levels, warnings and CPU temperature.
UPS-2 can be controlled by software commands from the Raspberry and/or by the on board push button. Supply commands include POWER OFF, STANDBY and RESTART.
- Compatible with Raspberry models 3, 3B, 4B and zero W
- High efficiency power supply with output 5V, 3A
- Main input voltage range 8V ... 18V
- Shutdown function with real power-off
- Battery standby current < 20uA @9V
- Battery voltage 6.5V ... 18V
- Nearly no self heating thanks to outstanding conversion efficiency
- Communication with Pi via serial UART or parallel port
- Python library for unattended operation and optional GUI

## Functions
### Hardware Control
#### Power Input Section
Input	Selection	Remark
Main	Selected if > 8V	Independent of battery voltage
Battery	Selected if main input < 7V	Battery voltage > 6.5V
Raspberry USB power input	Selected if present	Priority over Main and Batt inputs

#### LED Indicators
Input Voltage	White LED: Main	Blue LED: Battery
Voltage in range	ON	ON
Voltage low	BLINK	BLINK
No input	OFF	OFF

Raspberry State	Green LED *)	Raspberry Red LED
Complete power OFF	OFF	OFF
Standby (shut down)	OFF	ON
Starting up	BLINK FAST	ON
Run (up)	ON	ON
Shutting down	BLINK SLOW	ON

*) Green LED shows also feedback at push button operation

#### Push Button Operations
Push button allows manual invocation of different shut down and start up functions.
Button Operation	Function	Green LED
Short press	Start up from power off	fast blink
> 2 seconds	Shutdown to standby *)	> 2 blinks
> 5 seconds	Shutdown to power off **)	> 5 blinks
Double click	Shutdown and restart	slow blink -> fast blink

## Hardware Connections
#### UPS-2 Hat <> Raspberry-Pi Connections

  UPS-2 Hat connections

## Quick Start

## GUI-Graphical User Interface
Hyperlink to figure

## Software API

## Technical Data